## Slide 1: Review of the ecodesign regulation for water pumps Implementation questions and challenges associated with the Extended Product Approach (EPA) EELCF 29 Oct 2019

## Slide 2: Context : From component approach to Extended Product Approach
Current scope: ‘water pump’ = component = bare shaft pump = hydraulic part of a pump
  => Efficiency measured as MEI (Minimum Efficiency Index)
The extended product = hydraulic part + motor (+ VSD if any) = ‘water pump unit’
  Criterion = EEI (Energy efficiency index)
Pump
Bare shaft pump
Transmission
e.g. coupling
Electric
Motor
Electric
Motor
Desired work
Mains
Hydraulic circuit
System
Extended product
(‘water pump unit’ – EEI)
(VSD)
Current scope
(‘water pump’ – MEI)

## Slide 3: How to implement EPA to generate more savings ?
We propose to use EPA for pumps for which there is a clear benefit of using a VSD, i.e. for single stage pumps and booster sets
We propose to keep the current approach (MEI) for pumps for which there is no or uncertain benefit of using a VSD (e.g. multistage pumps)
The EEI requirement are set so that a VSD is needed to meet the requirement => this enables considerable energy savings in the system beyond the pump itself, through:
  Ensuring that load variations are achieved by adjusting motor speed rather than by destroying energy in throttling valves
  The use of a load profile with several load points, as representative as possible of real pump operation
  Reducing motor speed needs in case of oversized pump
  Adjusting the pump to the required load point via motor speed control rather than via pump trimming

## Slide 4: Implementation questions for the extended product approach:
General principle: when placed on the market, the extended product (pump unit = pump + motor + VSD if any) has to meet the EEIv requirements.
This approach allows significant energy savings but raises several important implementation questions and challenges, with different possible answers. Each answer has its pros and cons.
Answers in green below are those adopted in the draft Working Document. Questions in orange do not have an answer (yet) in the working document or relate to specific challenges.
Question 1:
Is it allowed to place a bare shaft pump on the market ? YES / NO
If yes, which requirement should apply:
- None
- Information requirements
- MEI
- EEIv calculated with default values for motor and VSD
- Indication ‘this pump must by driven by a VSD-fed motor’?
- Other ?

## Slide 5
Question 2:
Is it allowed to place a pump unit without VSD on the market ? YES / NO (because without VSD it does not meet the EEIv threshold and is not compliant)
If yes, which requirement should apply:
- Information requirements
- EEIv calculated with default values for VSD
- Indication ‘this pump unit must by driven by a VSD’
- Other ?
Question 3:
When a pump unit is placed on the market, which requirement should apply to the components?
  Motor: as per applicable requirements of the (revised) motors regulation when placed on the maket
  VSD: as per applicable requirements of the revised motors regulation when placed on the maket
  Bare shaft pump:
  - None
  - Information requirements only
  - as per applicable requirements of the (revised) pumps regulation when placed on the maket
  - Other ?

## Slide 6
Question 4:
What does it mean to place an extended product on the market ?
Supply the extended product as one integrated product: yes
Supply the extended product as part of a larger product/system: yes
Supply the pump and motor (and VSD) as separate components ?
  in the same box: no
  in a separate box in the same shipment: no
  in separate shipments: no
  Reasoning: if a motor and a pump are supplied together (even in the same box) does it necessarily mean that they are meant to form a pump unit together ?
  Challenge: These ‘no’ answers open a big loophole: to escape EEIv requirements is simple: one can supply pump and motor together, unmounted. Requirements would then apply when putting into service, which is much more difficult to verify (see question 7)
  Any suggestion to overcome the loophole ?
Supply the VSD as separate component of an assembled pump unit (motor + pump) ?
  in the same box: yes
  in a separate box in the same shipment: yes
  in separate shipments: no ?
  Reasoning: A VSD is often not physically attached to the rest of the pump unit. We need to provide this flexibility
  Challenge: For market surveillance purposes MSAs would have to verify that the VSD is indeed intended for the pump unit.

## Slide 7
Question 5:
Who is placing the ‘extended product’ on the market ?
Answer: The person making the extended product available for the first time on the EU market with a view to its distribution or use within the EU, whether for reward or free of charge and irrespective of the selling technique; (adapted from ecodesign directive).
It is thus the person who adds a motor (and VSD) to a bare shaft pump and places it on the market. It can be:
  The bare shaft pump manufacturer
  Pumps traders and suppliers
  OEMs
  Contractors that supply (part of) entire pump systems
  etc
  Challenges:
  There is a shift of responsibility. These economic operators need to be aware of their responsibility and capable to determine compliance and to issue DoC and apply CE mark.
  Market surveillance authorities are faced with a much broader range of economic operators
  Important role of pump suppliers to ‘educate’ their clients.

## Slide 8
Question 6
Where to put the nameplate and CE-mark on the extended product ?
We need to consider that:
Each component already has its own nameplate and CE-mark for its respective requirements as bare shaft pump, motor and VSD respectively
As indicated above, the extended product can supplied as separate components. How to indicate that together they meet the requirements ?
Any suggestion ?

## Slide 9
Question 7: How to enforce when the extended product is never placed on the market ?
This situation arises when the bare shaft pump + motor (+ VSD?) are supplied from different sources and assembled on site. Options:
Don’t enforce (risk of loophole)
Enforce when putting into service
This raises considerable challenges for enforcement and market surveillance:
Putting into service can be carried out by a vast number of different economic operators, including small installers or endusers, that need to be aware and capable to ensure compliance and issue DoC and CE mark
According to the blue guide, putting into service is a very specific moment, after which the regulation does not apply (the performance of the product may decrease due to e.g. poor operation & maintenance)
MSAs are not aware of where and when pumps are put into service.
Some MSAs do not have the legal powers to perform such on-site inspections.
Verifying compliance on paper can be rather straightforward, but actual testing the equipment that is about to be put into service is very challenging
In case of non compliance of the extended product when put into service, identification of the responsible person is tricky : non-compliance can due to low performance of any of the three components, due to poor combination, poor installation etc.
What are appropriate enforcement measures in case of non-compliance of the extended product when put into service ? Although the product is illegal (non-compliant) it seems hard and disproportionate to stop the production of a whole industrial plant because a small pump is non compliant.
Given the current resource availability of MSAs is it realistic to expect enforcement when putting into service ? How can we support enforcement when putting into service ?

## Slide 10
Question 8 :
What flexibility for spare parts ?
  Challenge (example): an industrial enduser urgently needs a pump unit (pump+motor) to replace a broken unit. Can he order a pump unit without the VSD ? If no, is it legal for him to discard the VSD and to install and put into service the pump unit without VSD ?